## Slide 1: AutonOmous Car

## Slide 2: Team:
Christoph Griesbeck
Christoph WinterW
Fabian Schurig
Ioannis Stratakos
Laurie Marceau
Roger Rösch
Valentin Novak
Yushen Zhang

## Slide 3: Goals:
Fully autonomous driving
Localization and navigation
Compliance with traffic signs
Compliance with traffic lights
Obstacle avoidance
Following lines

## Slide 4: Car:
Four wheel drive
Front and rear differential
Four independant suspension
High speed (very)
Two servo motors for steering
One big motor for driving

## Slide 5: System:
DE0-NANO FPGA Development Board
Sabre Lite i.MX6 Development Board
Two Ultrasonic Sensors
Logitech Quickcam Pro 9000
Homemade 3D stereo camera
GPS module

## Slide 7: Progress – System (Roger)
Compiled u-boot
Compiled Kernel
Setup phython server
Compiled OpenCV
Got OpenCL running
Raspberry Pi
Recording (FFMPEG)

## Slide 8: Progress – OPENCL
/usr/lib/libOpenCL.so:
undefined symbol: gcoOS_AtomConstruct

## Slide 9: Progress – controling the car:
FPGA <-> i.MX6 <-> PC GUI
Pwm (steering and acceleration)
Open loop regulation

## Slide 10: Progress – mechanical
Mounts
Wires and connectors
Cable managment

## Slide 11: Progress – GPS:
GPS reading (FPGA)
MAPS (Open street map)
Navigation (Osrm)

## Slide 12: Progress – Cameras:
Logitech (For traffic signs)
stereo (for lanes and obstacles)
320x240
25 FPS (Right light)
FFMPEG

## Slide 13: Progress – Cameras:

## Slide 14: Traffic Sign Detection - PROCEDURE (Christoph & Christoph)
Get the picture to analyse
Use HSV filter to select the relevant parts (e.g. red)
Use Canny alghorithm to detect edges
Apply findContours to get the shapes
Choose the relevant shapes
Check their properness in regard to possible signs
Return the located signs and their position

## Slide 15: Traffic Sign Detection – MILESTONES
Detect Stop signs
Detect priority signs
Detect red triangles (yield sign and warning sign)
Future - Get orientation of triangles
Future - Detect speed signs

## Slide 16: Traffic Sign Detection - RESULTS

## Slide 17: Traffic Sign Detection - RESULTS

## Slide 18: Line Detection - PROCEDURE (Fabian)
Get live video feed through LMS
Convert to Grey Image
Define region of interest 320x100
Use Canny Algorithm to detect edges
Find Contours with OpenCV
Approximate Polylines with Douglas Peucker Algorithm
Draw and output start and end points from each approximated polyline along the edge of a lane

## Slide 19: Line Detection – Missing
Interpretation of found polylines
Filter out everything except lanes
foresighted lines (looking ahead lines)

## Slide 20: Line Detection – RESULTS

## Slide 21: Line Detection - results
Polyline 1: Point(x,y)=586,1 Point(x,y)=638,61
Polyline 2: Point(x,y)=562,1 Point(x,y)=638,97

## Slide 22: Progress – Traffic Light Detection (Ioannis)
Calibration (Exact range of colors)
Transformation to HSV
Filter red, yellow and green
Locate circles (Hough algorithm)

## Slide 23: Progress – Issues and solutions
Car lights detected (Process only upper part)
Roads are not flat
Detecting non circular lights (vision algorithms)
Red and yellow light (experiment and optimization)

## Slide 24: Traffic Light Detection - Results

## Slide 25: Traffic Light Detection - Results

## Slide 26: Stereo Vision - PROCEDURE (Laurie)
Intrinsic calibration of camera

## Slide 27: Stereo Vision - PROCEDURE
Take picture
Remove distortion
Calculation of stereo dispartiy
Block matching algorithm

## Slide 28: Stereo Vision - Improvements
Real stereo camera
Extrinsic camera calibration
Real time depth mapping

## Slide 29: Stereo Vision - RESULTS

## Slide 30: Stereo Vision - RESULTS

## Slide 31: FUTURE WORK - odometry
Encoder (hard to install)
Inductive proximity sensor

## Slide 32: FUTURE WORK - TENTACLES
Has to be very fast
Has to adapt to car speed and properties